Communications Protocol of Hardware and Software LED control

Query:
  1. Send order:【0XEF】+【0X01】+【0X77】
  2. Controller response:
     【0X66】+【8bit device name(0x01)】+【8bit swtich on /off】+【8bit mode value】+【8bit run/pause state】+【8bit speed value】+【8bit red data】+【8bit green data】+【8bit blue data】+【0X00】+【0X99】
    1. 【8bit mode value】
      1. 0x25 ~ 0x38 is built-in mode,ps refer to “appendix1,built-in mode content”
      2. 0x39 is custom mode;
      3. 0x41 is static color mode;
    2. 【8bit swtich on /off】
      1. 0x23 is switch on
      2. 0x24 is switch off
    3. 【8bit run/pause state】(built-in mode、custom mode operative)
      1. 0x20 is run
      2. 0x21 is pause
    4. 【8bit speed value】(built-in mode、custom mode operative)
       Range:0x01--0x1F ,0x01 is the fastest,0x1F is the slowest;
2. Send static color:
  1. Send order:
     【0X56】+【8bit red data】+【8bit green data】+【8bit blue data】+【0XAA】
  2. Controller response:no response
3. Send built-in mode:
  1. Send order:
     【0xBB】+【8bit mode value】+【8bit speed value】+【0X44】
     【8bit mode value】Pls refer to “appendix1,built-in mode content”
     【8bit speed value】Range:0x01--0x1F ,0x01 is the fastest,0x1F is the slowest.
  2. Controller response:no response
4. Send command:switch on/off ;run/pause
  1. Send command:
     【0XCC】+【8bit key】+【0X33】
     【8bit key】
      1. 0x23 is switch on
      2. 0x24 is switch off
      3. 0x20 is run
      4. 0x21 is pause
  2. Controller response:no response

1. Send custom mode:
  1. Send command:
     【0X99】+【First point 24bit colorimetric value(R=?,G=?,B=?)】+【Second point 24bit colorimetric value】+【Third point 24bit colorimetric value】+【Fourth point 24bit colorimetric value】
     +【Fifth point 24bit colorimetric value】+【Sixth point 24bit colorimetric value】+【Seventh point 24bit colorimetric value】+【Eighth point 24bit colorimetric value】
     +【Ninth point 24bit colorimetric value】+【Tenth point 24bit colorimetric value】+【Eleventh point 24bit colorimetric value】+【Twelveth point 24bit colorimetric value】
     +【Thirteenth point 24bit colorimetric value】+【Fourteenth point 24bit colorimetric value】+【Fifteenth point 24bit colorimetric value】+【Sixteenth point 24bit colorimetric value】
     +【8bit speed value】+【8bit CHANGING mode value】+【0XFF】+【0X66】
    1. 【First point 24bit colorimetric value】
       are three bits which are three value of first RGB.There are total 16colors,then color value have 48 types.
    2. 【8bit CHANGING mode value】
      1. 0x3A :gradual
      2. 0x3B :jump;
      3. 0x3C :flash
    3. Notice:
       R=1,G=2,B=3 is a color terminator,it means this color is the last color.
  2. Controller response:no response
2. Other info:
  1. appendix1,built-in mode content:
1: 7 colors gradual change	0x25
2:red gradual change	0x26
3:green gradual change	0x27
4:blue gradual change	0x28
5:yellow gradual change	0x29
6:cyan gradual change	0x2A
7:purple gradual change	0x2B
8:white gradual change	0x2C
9:red and green gradual change	0x2D
10:red and blue gradual change	0x2E
11:green and blue gradual change	0x2F
12: 7 colors flicker	0x30
13:red flicker	0x31
14:green flicker	0x32
15:blue flicker	0x33
16:yellow flicker	0x34
17:cyan flicker	0x35
18:purple flicker	0x36
19:white flicker	0x37
20: jumpy 7 colors	0x38

  1. appendix2, colorimetric valuedefinition
【8bit red data】	0x00--0xFF
【8bit green data】	0x00--0xFF
【8bit blue data】	0x00--0xFF